## Slide 1
An Adaptive Hybrid Beamforming Approach for 5G-MIMO mmWave Wireless Cellular Networks
Domain: MATLAB
Technology: COMMUNICATION

## Slide 2: Index
Abstract
Introduction
Literature review
Existing Method
Disadvantages
Proposed method
Advantages
Applications
Hardware and Software Requirements
References

## Slide 3: Abstract
Hardware complexity reduction is a key concept towards the design and implementation of next generation broadband wireless networks. To this end, the goal of the study presented in this paper is to evaluate the performance of an adaptive hybrid analog-digital beamforming approach in fifth-generation (5G) massive multiple input multiple output (MIMO) millimeter wave (mmWave) wireless cellular orientations. In this context, generated beams are formed dynamically according to traffic demands, via an on-off analog activation of radiating elements per vertical antenna array, in order to serve active users requesting high data rate services without requiring any expensive and mechanical complex steering antenna system. Each vertical array, which constitutes a radiating element of a circular array configuration, has a dedicated radio frequency chain (digital part). The performance of our proposed approach is evaluated statistically, by executing a sufficient number of independent Monte Carlo simulations per MIMO configuration, via a developed systemlevel simulator incorporating the latest 5G-3GPP channel model. According to the presented results, the adaptive beamforming approach can improve various key performance indicators (KPIs) of the wireless orientation, such as total downlink transmission power and blocking probability. In particular, when studying/analyzing a MIMO configuration with 15 vertical antenna arrays and10 radiating elements per array, then, depending on the tolerable amount of transmission overhead, the proposed adaptive algorithm can significantly reduce the number of active radiating antenna elements compared to the static grid of beams case. In the same context, when keeping the number of radiating elements constant, then the total downlink transmission power as well as the blocking probability can be significantly reduced. It is important to note that all the KPIs have been extracted when deploying the developed array configuration in complex cellular orientations (two tiers of cells around the central cell).

## Slide 4: Introduction:
The provision of zero latency high data rate services to mobile consumers is intrinsically linked with a comprehensive network redesign as the deployment of fifth-generation (5G) broadband wireless cellular networks approaches reality [1]. In this regard, several cutting-edge technologies have been launched to serve the 5G vision, including massive multiple input multiple output (MIMO) designs [6]–[7], non-orthogonal multiple access (NOMA), and millimeter wave (mmWave) transmission. In the latter scenario, several antenna arrays are installed at cellular orientation base stations (BSs) to serve mobile stations (MSs) that are requiring high data rate services. The creation of highly directed beams that reduce multiple access interference allows for this (MAI).

## Slide 5: Literature review:
S. NO | Journal Type with year | Authors | Title | Outcomes
1 | vol. 23, no. 2, pp. 668-695. | S. Haykin | “A survey on resource allocation for 5G heterogeneous networks” | Studied about the 5g Heterogeneous networks
2 | IEEE Access, vol. 8, pp. 62367-62414, Mar. 2020. | B. U. Kazi and G. A. Wainer, | “A comprehensive survey on millimeter wave communications for fifth-generation wireless networks: Feasibility and challenges,” | Studied about millimeter Wave communication for 5g.
3 | IEEE Access, vol. 8, pp. 62367-62414, Mar. 2020. | Y. Ye, Y. Li, G. Lu, and F. Zhou | “Opportunities and challenges of mmWave NR,” | Studied about opportunities and challenges of Millimeter Wave.
4 | vol. 1, pp. 179-189, Jan. 2020. | N. A. El-Alfi, H. M. Abdel-Atty, and M. A. Mohamed | “A survey of NOMA: Current status and open research challenges,” | Studied about the NOMA
5 | IEEE Access, vol. 7, pp. 88743-88755, Jul. 2019. | L H. V. Poor and O. Hadjiliadis, | “Flex-NOMA: Exploiting buffer-aided relay selection for massive connectivity in the 5G uplink,” | Learned about NOMA Exploiting Buffer.

## Slide 6: Existing method:
In order to show the features of RA models in traditional HetNets, we use an uplink heterogeneous macro-femto network as an example. Assume there is one MBS serving F MUs and one FBS serving K FUs. The number of MUs and FUs is defined as ∀f ∈ {1,..., F} and ∀k, i ∈ {1,..., K}, respectively. Under this network, the key problem is to design the power allocation (PA) strategy of FUs under certain objective functions and constraints. For example, the RA problem can be formulated as the sum-rate maximization problem of all FUs by optimizing the transmit power of each FU subject to the minimum SINR/rate constraint of FU, the cross-tier
where pk and pi are the transmit power of FU k and FU i, respectively. hk is the channel gain from FU k to the FBS. hi,k is the interference channel gain from FU i. Pf and gf ,k denote the transmit power of MU f and the interference channel gain from MU f. σ2 is the background noise power.
Accordingly, the data rate of FU k is Rk = log2(1 + rk ). From (1), pk and pi are coupled in rk , so that the sum rate k Rk is non-convex. If the objective function becomes the total power minimization, the formulated objective function is convex. If the objective function becomes the EE maximization (e.g., k Rk k pk +pc ), it belongs to a fractional programming (FP) problem. Where pc is the circuit power consumption. Thus, we require to convert it into a convex form. As a result, for different RA problems, it is difficult to use one common approach to deal with it. Moreover, for different transmission modes (uplink/downlink), the maximum transmit power constraint is different. Under an uplink mode, the transmit power of FU is limited by its own peak power constraint. However, for a downlink mode, the allocated power from the FBS to each FU is limited by the sum power constraint at the BS.

## Slide 7: Existing methods:
Accordingly, the data rate of FU k is Rk = log2(1 + rk ). From (1), pk and pi are coupled in rk , so that the sum rate k Rk is non-convex. If the objective function becomes the total power minimization, the formulated objective function is convex. If the objective function becomes the EE maximization (e.g., k Rk k pk +pc ), it belongs to a fractional programming (FP) problem. Where pc is the circuit power consumption. Thus, we require to convert it into a convex form. As a result, for different RA problems, it is difficult to use one common approach to deal with it. Moreover, for different transmission modes (uplink/downlink), the maximum transmit power constraint is different. Under an uplink mode, the transmit power of FU is limited by its own peak power constraint. However, for a downlink mode, the allocated power from the FBS to each FU is limited by the sum power constraint at the BS.

## Slide 8
Disadvantages in Existing method:
In traditional multi-user (MU) MIMO systems, fully digital (FD) precoding is the typical approach to adjust the amplitudes and phases of the transmitted signals in order to achieve optimum beamforming. However, in a massive MIMO configuration, FD approach would result in a significant computational and hardware burden, since the number of radio frequency (RF) chains is equal to the number of antennas.

## Slide 9: Proposed method:
The studied adaptive beamforming approach is described in Table I. In this context, the set b denotes the active radiating elements of the array geometry deployed in the b th BS and b the corresponding angles of the generated adaptive beams (notation a:b indicates all elements from a to b with step 1). Moreover, each entry of Hk k s ,sec( ), (indicating the channel matrix of the k th MS relevant to its serving sector for the s th PRB) is calculated according to (2). In addition, x represents the eigenvector corresponding to the maximum eigenvalue of matrix H H H k k s k k s ,sec( ), ,sec( ), , SNRk is the signal to noise ratio of the k th MS with respect to all available PRBs of the b th BS (i.e., b ) and TLk,sec(k),s, CGk,s represent the total losses and the channel gain, respectively, of the k th MS relevant to the s th PRB. Finally, the minimum required SNR for acceptable QoS and the thermal noise level at the receiver are denoted by SNRth and Io, respectively. Note that during subcarrier allocation (line 3), function sort(SNRk,Rk) sorts the values in vector matrix SNRk in descending order and returns the first Rk sorted values as well as the corresponding indexes (assigned to set k ).

## Slide 10: Proposed method:
In the initial state, it is assumed that an arbitrary BS employs a FGoB, where three active sectors have a spatial separation of 120o (e.g., Fig. 5(a)). To this end, the deployed geometry is defined according to the angle of the first MS which is served by this BS. Assuming that in this case the vertical array vo is activated, then two additional arrays, and in particular vo + [v/3] and vo+2[v/3] are activated as well, in order to provide the necessary 120o separation in the deployed beams. Once a potential (new) MS requesting Rk PRBs tries to enter the network, it is examined if the minimum required transmission power for acceptable QoS can be provided from the already deployed geometry without power outage. If this is true, then this MS is accepted in the network and all equivalent parameters are updated (MS is served by the l th beam which is generated by the vk vertical array, line 8). However, in the opposite case (line 9), the beam can be steered to an adjacent angular location (e.g., Fig. 5(b - g)). This is achieved by the activation of a different vertical array, according to the angular position of the potential new MS (lines 11-14 in Table I and blue arrows in Fig. 5 that indicate the adjacent vertical arrays). Note that in this case all radiating elements of this array are activated. If however power outage occurs in at least one of the already served MSs of this BS, then all radiating elements in the initial vertical arrays (as defined in line 1) can be activated, thus providing a grid of beams with increased gain (Fig. 5(h), line 19 in Table I

## Slide 11: Proposed method:
In all the aforementioned cases where antenna radiation pattern modification takes place, it is examined if the considered alterations in the radiation diagram will result in link outage for another of the already served MSs by the b th BS (e.g., lines 16 and 21), as it was previously explained. If this is true even in the case where all radiating elements per vertical array are activated (Fig. 5(h)), or the considered MS cannot be provided with acceptable QoS, then reject flag (rf) is set to 1 and the process is repeated for the next candidate MS. Otherwise, corresponding sets (i.e., b and b ) are updated. Finally, as also mentioned in Section II, each MC run comes to an end either when the transmission power of the b th BS (denoted as Pt,b) exceeds a predefined threshold (Pm) or lack of available PRBs takes place. The first set of simulation results is presented in Figs. 6-8 for the considered antenna geometries of Fig.4 (FGoB). In all figures, cumulative distribution function (CDF) curves have been plotted versus each of the considered KPIs of Section II. Since adaptive modulation and coding per subcarrier is outside the scope of our study, we consider two distinct values for the requested transmission rate, common for all MSs (i.e., Rk = R), which is can be satisfied with a proper assignment of PRBs and modulation order per PRB. In this context, in all simulation scenarios either 5 or 15 PRBs can be allocated to a potential MS, thus equivalent bit rates of 7.2/21.6 Mbps can be supported (i.e., the product of the assigned PRBs per MS, the subcarriers per PRB, the subcarrier spacing, as well the transmitted bits per subcarrier as defined by the modulation.
Moreover, wireless orientations with two tiers of cells around the central cell have been considered. All simulation parameters are summarized in Table II, which are aligned with the majority of related works in [44]. Finally, in each figure legend, notation (v,w,R) has been considered. Since all vertical arrays are activated, the term active beams will be used as well throughout the rest of this subsection to indicate the number of generated beams per BS.

## Slide 12: Proposed method:
Total Throughput = assigned_PRBs_perMS*Nu*PRB
Transmission Power
Nu = Number of users
Max_tx_PoWhere,
Throughput = Data that can be transferred by the network
assigned_PRBs_perMS = assigned Physical Resource Blocks per Mobile Station or user
PRB = Physical Resource Blocks
Pt = Nu*Max_tx_Power_BSperMS
Where,
Pt = Totalwer_BSperMS = Maximum Transmission Power of Base Station that can be consumed per Mobile

## Slide 13: proposed method adaptive beam forming

## Slide 14: Advantages of Proposed method:
Improved spectral efficiency
Reduced power consumption
Reduced interference
Increased range

## Slide 15: Applications of Proposed method:
Mobile communication
Internet of Things (IoT)
Smart cities
Virtual reality (VR) and augmented reality (AR)

## Slide 16: Hardware and Software Requirements:
Hardware & Software Requirements:
Software: Matlab R2018a.
Hardware:
Operating Systems:
• Windows 10
• Windows 7 Service Pack 1
• Windows Server 2019
• Windows Server 2016
Processors:
Minimum: Any Intel or AMD x86-64 processor
Recommended: Any Intel or AMD x86-64 processor with four logical cores and AVX2 instruction set support
Disk:
Minimum: 2.9 GB of HDD space for MATLAB only, 5-8 GB for a typical installation
Recommended: An SSD is recommended a full installation of all Math Works products may take up to 29 GB of disk space
RAM:
Minimum: 4 GB
Recommended: 8 GB

## Slide 17: References:
1. Y. Xu, G. Gui, H. Gacanin and F. Adachi, “A survey on resource allocation for 5G heterogeneous networks: Current research, future trends, and challenges,” IEEE Commun. Surv. Tutor., vol. 23, no. 2, pp. 668-695, Secondquarter 2021.
2. A. N. Uwaechia and N. M. Mahyuddin, “A comprehensive survey on millimeter wave communications for fifth-generation wireless networks: Feasibility and challenges,” IEEE Access, vol. 8, pp. 62367-62414, Mar. 2020.
3. A. V. Lopez, A. Chervyakov, G. Chance, S. Verma and Y. Tang, “Opportunities and challenges of mmWave NR,” IEEE Wirel. Commun., vol. 26, no. 2, pp. 4-6, Apr. 2019.
4. B. Makki, K. Chitti, A. Behravan and M. -S. Alouini, “A survey of NOMA: Current status and open research challenges,” IEEE OJ-COMS, vol. 1, pp. 179-189, Jan. 2020.
5. N. Nomikos, E. T. Michailidis, P. Trakadas, D. Vouyioukas, T. Zahariadis and I. Krikidis, “Flex-NOMA: Exploiting buffer-aided relay selection for massive connectivity in the 5G uplink,” IEEE Access, vol. 7, pp. 88743-88755, Jul. 2019.